## Slide 1: Measurement of electron number per pulse in UED set up
Jaewon Yun

## Slide 2: Goal
Accurately measure the electron number per pulse.
3 methods:
Faraday cup
Sum pixel intensity from the CCD
Particle simulations

## Slide 3: Why is it important to determine electron number per pulse?
1. More electrons will produce brighter diffraction image
2. It is convention to report the number of electrons for each diffraction images

## Slide 4
Ultrafast electron diffraction layout
Detector
CCD Camera

## Slide 5: Faraday Cup
All units in mm

## Slide 6: Picture of the Faraday Cup inside the vacuum chamber
Picture of the vacuum chamber

## Slide 7
CCD Camera
Quad-RO_4320

## Slide 8: Picture of electron beams (110kV)
97.5 μW
190.5 μW
255 μW
349.5μW
448 μW
561 μW
656 μW
780 μW
Camera Exposure time : 0.2 second
Each image is the average intensity profile of 10 frames

## Slide 9: General Particle Tracer Simulation
General Particle Tracer simulates the behavior of an electron beam as it travels from the photocathode through aperture at anode and all the way through the Camera.
It considers the space charge effect and relativistic effect.

## Slide 10
30kV
60kV
90kV
120kV

## Slide 11
Chart: Laser power vs Net intensity (CCD Camera)
| 780 | 656 | 561 | 448 | 349.5 | 255 | 190.5 | 97.5 | 50
-110kV | 115737928 | 93949699 | 96976820 | 54348422 | 29006648 | 10813073 | 6774325 | 1043858 | 60077
-90kV | 2562479 | 5057097 | 25600470 | 35588602 | 50321205 | 61102001 | 90698093 | 108284219 | 117043270
-60kV | 102557779 | 106649884 | 37000052 | 19336377 | 7250197 | 212403 | 13202
-30kV | 55691936 | 42338342 | 35314425 | 27344177 | 17390403 | 16335953 | 3843443 | 1665627 | 406174

## Slide 12
Chart: 2019.Nov.8 Faraday Cup:
| 329 | 305 | 286 | 260 | 236 | 217 | 195 | 175 | 165 | 147 | 132 | 123 | 105 | 89
-100kV | 76 | 641 | 865 | 1508 | 2300 | 2980 | 3709 | 4122 | 2986 | 2141 | 2383 | 1154 | 558 | 74
-90kV | 476 | 1118 | 1517 | 1601 | 2202 | 2560 | 2724 | 2212 | 1760 | 1144 | 1256 | 377
-85kV | 166 | 472 | 1119 | 1865 | 1545 | 1566 | 1949 | 2298 | 2488 | 2509 | 2326 | 2121 | 1533 | 1448 | 612 | 267 | -251
-60kV | 273 | 880 | 1315 | 2069 | 1344 | 1575 | 1625 | 1652 | 1123 | 221

## Slide 13
Chart: 2019.Dec.9th Faraday Cup:
| 0.16800000000000001 | 0.155 | 0.13400000000000001 | 0.125 | 0.11700000000000001 | 0.10299999999999999 | 9.6000000000000002E-2 | 8.1000000000000003E-2 | 6.9000000000000006E-2 | 5.3999999999999999E-2 | 3.2000000000000001E-2 | 0.01
-100kV | 2484.1206 | 2421.7055 | 3108.2715 | 3482.7621 | 4106.913 | 4169.3281 | 4044.4979 | 3201.8942 | 2402.981 | 923.7434 | 156.0377 | 93.6226
-90kV | 49.9321 | 131.0717 | 636.6339 | 2359.2905 | 3295.5168 | 4106.913 | 4169.3281 | 4106.913 | 4106.913 | 3420.347 | 2296.8754 | 1984.7999
-75kV | 2484.1206 | 2858.6112 | 3982.0828 | 4106.913 | 4163.0866 | 3982.0828 | 3794.8376 | 3108.2715 | 2047.215 | 611.6679 | 112.3472 | 68.6566
-60kV | 1797.5546 | 1953.5924 | 2296.8754 | 2671.3659 | 2796.1961 | 2921.0263 | 2733.781 | 2172.0452 | 1485.4792 | 486.8377 | 112.3472 | 49.9321
-45kV | 1797.5546 | 1922.3848 | 1235.8188 | 1173.4037 | 1167.1622 | 986.1584 | 736.4981 | 611.6679 | 405.6981 | 174.7623 | 93.6226 | 74.8981

## Slide 14
Chart: 2019.Dec.10th Faraday Cup:
| 0.14499999999999999 | 0.13400000000000001 | 0.123 | 0.11700000000000001 | 0.10299999999999999 | 9.7000000000000003E-2 | 8.2000000000000003E-2 | 7.0000000000000007E-2 | 5.1999999999999998E-2 | 3.2000000000000001E-2 | 0.01
-100kV | 2559.0187 | 2683.8489 | 3307.9998 | 3370.4149 | 3495.2451 | 3183.1697 | 2059.698 | 998.6415 | 218.4528 | 56.1736 | 31.2075
-90kV | 2122.1131 | 2184.5282 | 2371.7735 | 2434.1886 | 2559.0187 | 2496.6037 | 1747.6226 | 936.2264 | 249.6604 | 43.6906 | 37.4491
-75kV | 2184.5282 | 2683.8489 | 3120.7546 | 3476.5206 | 3557.6602 | 3495.2451 | 2808.6791 | 1841.2452 | 474.3547 | 81.1396 | 37.4491
-60kV | 1423.0641 | 1248.3018 | 1872.4527 | 2371.7735 | 2871.0942 | 3120.7546 | 3744.9055 | 3807.3206 | 3183.1697 | 873.8113 | 49.9321
-45kV | 2115.8716 | 1622.7924 | 1685.2075 | 1872.4527 | 2122.1131 | 2246.9433 | 2496.6037 | 2808.6791 | 2434.1886 | 1373.132 | 24.966

## Slide 15
1000
10000
20000
50000
5000

## Slide 16
Chart: Voltage vs Net intensity(Laser power 630μW -Max Power)(CCD Camera)
| 80 | 110 | 100 | 70 | 60 | 50 | 10 | 20 | 30 | 40 | 90
 | 110406329 | 113928391 | 117988312 | 117973655 | 112257904 | 98494621 | 6961212 | 25192613 | 51038563 | 79899634 | 117043270

## Slide 17
Chart: Voltage vs electrons per pulse (Laser power 165μW) (Faraday Cup )
| 95 | 90 | 85 | 80 | 75 | 70 | 65 | 60 | 55 | 50 | 45 | 40 | 35 | 30 | 25 | 20 | 15
 | 3086 | 3072 | 2738 | 2777 | 2570 | 2377 | 2126 | 2180 | 1995 | 1816 | 1497 | 1339 | 1135 | 988 | 687 | 439 | -30

## Slide 18: Future Direction
Redo the Faraday Cup measurement and sum intensity camera measurement with adjusted laser position and adjusted Faraday Cup position for each measurement.
Long term work is to wait for the laser to be fixed and redo the measurement

## Slide 20
Chart: 2019.Nov.8 Voltage vs electrons per pulse (Laserpower 165μW)
| 95 | 90 | 85 | 80 | 75 | 70 | 65 | 60 | 55 | 50 | 45 | 40 | 35 | 30 | 25 | 20 | 15
 | 3086 | 3072 | 2738 | 2777 | 2570 | 2377 | 2126 | 2180 | 1995 | 1816 | 1497 | 1339 | 1135 | 988 | 687 | 439 | -30
Chart: Voltage vs Net intensity(Laser power 630μW -Max Power)
| 80 | 110 | 100 | 70 | 60 | 50 | 10 | 20 | 30 | 40 | 90
 | 110406329 | 113928391 | 117988312 | 117973655 | 112257904 | 98494621 | 6961212 | 25192613 | 51038563 | 79899634 | 117043270

## Slide 21: Comparison
Chart: Laser power[μW]
| 56 | 94 | 163 | 210 | 296 | 370 | 480.5 | 600 | 630
90kV Nov22nd | 2562479 | 5057097 | 25600470 | 35588602 | 50321205 | 61102001 | 90698093 | 108284219 | 117043270
110kV Nov20th | 115737928 | 93949699 | 96976820 | 54348422 | 29006648 | 10813073 | 6774325 | 1043858 | 60077
30kV Nov20th | 55691936 | 42338342 | 35314425 | 27344177 | 17390403 | 16335953 | 3843443 | 1665627 | 406174
60kV Nov19th | 102557779 | 106649884 | 37000052 | 19336377 | 7250197 | 212403 | 13202
Chart: Laser power [μW]
| 380 | 308 | 274 | 265 | 255 | 247 | 227 | 201 | 182 | 170 | 157 | 143 | 135 | 125 | 108 | 98 | 76
85kV | 166 | 472 | 1119 | 1865 | 1545 | 1566 | 1949 | 2298 | 2488 | 2509 | 2326 | 2121 | 1533 | 1448 | 612 | 267 | -251
100kV | 76 | 641 | 865 | 1508 | 2300 | 2980 | 3709 | 4122 | 2986 | 2141 | 2383 | 1154 | 558 | 74
60kV | 273 | 880 | 1315 | 2069 | 1344 | 1575 | 1625 | 1652 | 1123 | 221
90kV | 476 | 1118 | 1517 | 1601 | 2202 | 2560 | 2724 | 2212 | 1760 | 1144 | 1256 | 377

## Slide 22
2019.Nov.8 (maximum number of electrons were detected)
Standard deviation :448
Maximum value :5499
Minimum value :3133
Mean value :4122

## Slide 23: Case for 100kV

## Slide 24: Estimating Beam size (CCD Camera)
Chart: Laser power vs Electron beam spot size (FWHM) for -110kV
| 780 | 656 | 561 | 448 | 349.5 | 255 | 190.5 | 97.5
 | 1.7016 | 1.5552 | 1.8456 | 1.7364 | 1.5804 | 1.0164 | 0.9588 | 0.8688

## Slide 25
Chart: Laser power vs Electron beam spot size (FWHM) for 110kV
| 780 | 656 | 561 | 448 | 349.5 | 255 | 190.5 | 97.5
 | 1.7016 | 1.5552 | 1.8456 | 1.7364 | 1.5804 | 1.0164 | 0.9588 | 0.8688